CO2020- Computer Aided Numerical Methods
HomeWork 5 – Parabolic PDEs

Ishaan Jain
CO21BTECH11006

Ans1.
(a)

vec nabla = partial over {partial x} hat e_x + partial over {partial y} hat e_y + partial over {partial z} hat e_z = α partial over {partial r} hat e_r + β partial over {partial θ} hat e_θ + partial over {partial z} hat e_z

We know that,
{partial}over{partial r} = x_r {partial}over{partial x} + y_r {partial} over {partial y}	eqn(i)
{partial}over{partial θ} = x_θ {partial}over{partial x} + y_θ{partial} over {partial y}	eqn(ii)
where, x = r cos θ and y = r sin θ ,
On calculating, x_r = cos θ , y_r = sin θ , x_θ = -r{sin θ} and y_θ = r{cos θ}

And the unit vectors are defined as:

hat e_r = cos θ hat e_x + sin θ hat e_y and hat e_θ = hat e_z times hat e_r = -sin θ hat e_x + cos θ hat e_y

Substituting in the first equation,
α partial over {partial r} = cos θ partial over {partial x} + sin θ partial over {partial y}	eqn(iii)
β partial over {partial θ}= - sin θ partial over {partial x} + cos θ partial over {partial y}	eqn(iv)

from i, ii, iii and iv,
α (cos θ partial over {partial x} + sin θ partial over {partial y }) = cos θ partial over {partial x} + sin θ partial over {partial y} drarrow α = 1
β (-r sin θ partial over {partial x} + r cos θ partial over {partial y}) = - sin θ partial over {partial x} + cos θ partial over {partial y} drarrow β = 1 over r

i.e.
vec nabla = partial over {partial r} hat e_r + 1 over {r} partial over {partial θ} hat e_θ + partial over {partial z} hat e_z

To solve the continuity equation,
vec nabla. vec v = 0
vec nabla. vec v = {partial v_r} over {partial r} + 1 over {r} {partial v_θ} over {partial θ} hat e_θ + {partial v_z} over {partial z} hat e_z + v_r (nabla.hat e_r) + v_θ(nabla . hat e_θ) + v_z(nabla.hat e_z)

nabla .e_z = 0
nabla . e_r = nabla.(cos θ e_x + sin θ e_y) = -sin θ {partial θ} over {partial x} + cos θ {partial θ} over {partial y} = -sin θ (-sinθ over r) + cos θ ({cos θ} over r) = 1 over r
and
nabla . e_θ = nabla.(-sin θ e_x + cos θ e_y) = -cos θ {partial θ} over {partial x} - sin θ {partial θ} over {partial y} = -cos θ (-sinθ over r) - sin θ ({cos θ} over r) = 0

Hence, nabla. vec v = {partial u_r} over {partial r} + 1 over {r}{partial u_θ} over {partial θ} + {partial u_z} over {partial z} + u_r over r

In 2D, we can neglect z-axis term;
So the final equation becomes:
nabla. vec v = {partial u_r} over {partial r} + 1 over {r}{partial u_θ} over {partial θ} + u_r over r

(b) The Gradient operator in Cylindrical coordinates we already defined and proved in the last part, using that result:

nabla ^2 T = vec nabla. (vec nabla T)= (partial over {partial r} hat e_r + 1 over {r} partial over {partial θ} hat e_θ + partial over {partial z} hat e_z ).({partial T} over {partial r} hat e_r + 1 over {r} {partial T} over {partial θ} hat e_θ + {partial T} over {partial z} hat e_z )

nabla^2 = {partial ^2 T}over{ partial r^2} + 1 over r partial over {partial θ} left(1 over r {{partial T} over {partial θ}} right) + {partial^2 T}over {partial z^2} + 1 over r { partial T} over {partial r}

nabla^2 T = {partial ^2 T}over{ partial r^2} + 1 over r^2 {partial^2 T} over {partial θ^2} + {partial^2 T} over {partial z^2} + 1 over r {partial T}over{partial r}
### We can neglect the z axis for 2D form:
nabla^2 T = {partial ^2 T}over{ partial r^2} + 1 over r^2 {partial^2 T} over {partial θ^2} + 1 over r {partial T}over{partial r}

Ans 2.
(a) The stencils for i = 0 and i = n_x - 2 are calculated the by the following taylor series expansion:
T_0 = T_1 - Δ x T'_1 + left( Δx^2 over 2right)T''_1 - left( Δx^3 over 6 right)T'''_1 + left( Δx^4 over 24 right)T''''_1 + O(Δx^5 )
T_2 = T_1 + Δ x T'_1 + left( Δx^2 over 2right)T''_1 + left( Δx^3 over 6 right)T'''_1 + left( Δx^4 over 24 right)T''''_1 + O(Δx^5 )
T_3 = T_1 +2 Δx T'_1 + left( (2Δx)^2 over 2right)T''_1 + left( (2Δx)^3 over 6 right)T'''_1 + left( (2Δx)^4 over 24 right)T''''_1 + O(Δx^5 )
T_4 = T_1 + 3Δx T'_1 + left( (3Δx)^2 over 2right)T''_1 + left( (3Δx)^3 over 6 right)T'''_1 + left( (3Δx)^4 over 24 right)T''''_1 + O(Δx^5 )

left[matrix{T_0 - T_1 ## T_2 - T_1 ## T_3 - T_1 ## T_4 - T_1}right] = left[matrix{-1# 1/2# -1/6 #1/24 ## 1# 1/2# 1/6 #1/24 ## 2 # 2 # 4/3 # 2/3 ##3 # 9/2 # 9/2 # 27/8}right] left[matrix{ ΔxT'_1 ## Δx^2 T''_1 ## Δx^3 T'''_1 ##Δx^4 T''''_1}right]
b = Ax drarrow A^-1 b = x
Find the inverse and find the second row which will give the value of T''_1 .
Similarly find the right stencil at i = nx-2.
The values calculated are implemented in the code.
(b) Von-Neumann stability analysis:
r = k Δt over Δx^2
T_j ^n = z^n e^{ijθ} where n in the time instance and j is the position.
T_j^{n+1} - T_j^n = r (T_{j+1}^n - 2T_j^n + T_{j-1}^n)
z^{n+1}e^{ijθ} - z^{n}e^{ijθ} = r (z^{n}e^{i(j+1)θ}- 2 z^{n}e^{i(j)θ} + z^{n}e^{i(j-1)θ})
z - 1 = r (e^{iθ}- 2 + e^{-iθ})
z = 1 - r (2 - 2 cos θ )
For The analysis to be stable,
-1 leslant z leslant 1 drarrow -1 leslant 1-2r(1-cos θ) leslant 1
-1 leslant -r(2 sin^2 (θ/2)) leslant 0
0 leslant r leslant 1/{2sin^2 (θ/2)}
 In limiting case, r holds it’s maximum value as r = 1/2
at r = 0.5, 0.5 = k Δt over Δx^2 drarrow 0.5 = 10^-4 over Δx^2
Δx = sqrt {2 times 10^-3} = 0.0141421
number of partitions = {1-0} over Δx = 70 at which the system is stable. After this the error starts growing.
There may be an error in calculations because for me, after n = 62, error is starting to grow.

(c)

The graph above is the error vs nx plot for two different time intervals.
Initially, the log-log values are parallel to the straight line with slope = -4.
for second case, after nx = 350 (approx), the error starts to grow and we see a asymptotic curve in our plot.